## Slide 1
Film Digitization System
Software Pipeline: Scan · Stitch · Post-Process
ECE 445 · Raspberry Pi HQ Camera (IMX477) · STM32 MCU · Gemini AI

## Slide 2
OVERVIEW
Software Pipeline Architecture
01
SCAN
RPi HQ Camera captures overlapping tiles; STM32 steps motorized film gate on each exposure
02
STITCH
Feather-blend 40 tiles into a seamless full-frame mosaic using manifest-driven weight maps
03
PROCESS
Density-domain negative inversion + perceptual tone mapping + Gemini-driven iterative refinement
04
OUTPUT
Social-media-ready JPEG + metadata JSON report; cloud upload via AWS S3 + Lambda
Hardware: STM32 MCU controls dual LED arrays (backlight / frontlight) and motorized film gate

## Slide 3
STAGE 01 — SCANNING
Tile Capture & Coordination
1
Browser sends POST /scan → FastAPI server.py triggers job
server.py
2
ScanJobCoordinator starts background thread; state machine: Ready → Working
coordinator.py
3
STM32 steps film gate; RPi HQ Camera captures each tile (IMX477, 12 MP)
serial_comm.py · MockSerialInterface fallback for dev
4
Each tile saved with row/col position metadata to manifest.csv
tiles/ + manifest.csv
5
Frontend polls GET /status at 500 ms; receives state + output URLs on done
software/web/app.js
40-tile capture grid (5 × 8)
← overlap region (feather zone)

## Slide 4
STAGE 02 — STITCHING
Feather-Blended Tile Assembly
Weighted Pixel Accumulation
Overlap zone: linear weight ramp ε → 1.0 → ε
Non-overlap zone: weight = 1.0
output = Σ(pixel × weight) / Σ(weight) → seamless seams
manifest.csv Schema
row, col, filename, left, top, right, bottom, overlap_x_px, overlap_y_px
Tile positions define exact pixel placement on the full-frame canvas
Post-Stitch Enhancement Stages
Invert (255 − pixel)
White Balance (per-channel percentile gain)
Auto-Levels → CLAHE (LAB L-channel)
Cast-suppression mask → Selective Desaturation
Unsharp Mask (σ=1.2, amount=0.35)
Weight profile across tile boundary:
Tile 1
Tile 2
ramp
Tile 3
ramp
weight = 1.0
ramp
weight = 1.0
ramp
weight = 1.0
← Tile A · Overlap · Tile B · Overlap · Tile C →
Output Files
stitched_raw.png
inverted_positive.png
white_balanced.png · leveled.png
desaturation_mask.png
processed_negative.png ← final

## Slide 5
THE CORE CHALLENGE
Why Negatives Are the Hardest Problem
Orange Mask
Film base has a deep orange coupler dye
Varies by brand, age, and chemistry
Must be estimated from clear-base ROI
Incorrect removal destroys color accuracy
Inverted Tones & Dye Crosstalk
Cyan/Magenta/Yellow dyes record complements
Simple 255−x inversion creates severe casts
Dye channels bleed into each other
Must invert in optical-density space
Non-linear Tone & Gamma
Film gamma ≠ digital display gamma
Shadow/highlight zones behave non-linearly
Perceptual tone mapping required (LAB)
Auto-levels alone → flat, desaturated result

## Slide 6
STAGE 03 — NEGATIVE INVERSION
Density-Domain Inversion Pipeline
①
Base
Correction
frame ÷ base_rgb
clips transmission
to (ε, 1]
②
Density
Calc
density =
−log(transmission)
per channel
③
Dye
Unmixing
3 × 3 matrix
separates CMY
dye channels
④
Expm1
Invert
(eˣ − 1) ×
gains
[1.35, 1.20, 1.10]
⑤
Color
Mapping
gray anchor +
empirical 3×3 +
neutral damp
Key Insight: Optical Density Space
OD = −log(light transmission through film)
Dye concentrations add linearly in OD (Beer-Lambert)
Preserves color relationships across exposures
Simple RGB inversion breaks this — OD space fixes it
Conservative Dye Unmixing Matrix
[ 1.55 −0.38 −0.17 ]
[ −0.22 1.44 −0.22 ]
[ −0.08 −0.45 1.53 ]
Blended with identity matrix by strength

## Slide 7
STAGE 03 — PHYSICAL RAW PIPELINE
RAW-First 10-Stage Correction
DNG
RAW Bayer Ingest
rawpy loads .dng; extracts Bayer mosaic + black/white level metadata → float32
S1
Flat-Field Correction
Multi-scale Gaussian models backlight illumination map per CFA plane; corrected = frame ÷ illum^strength
S2
Demosaic → RGB
Bilinear Bayer interpolation → linear float32 RGB; diagnostic preview saved
S3
Base Reference Extraction
Median RGB of clear-base ROI (p10–p90 luma) from reference_layout.json
S4
Base Correction + Density
frame ÷ base_rgb → transmission; −log(T) → optical density; percentile normalize
S5
Dye Unmixing
3×3 matrix in density domain blended with identity; separates CMY channels
S6
Expm1 Inversion
(eˣ − 1) × per-channel gains [1.35, 1.20, 1.10] → positive image
S7
Soft Reference Mapping
Gray anchor (0.35) → empirical 3×3 → neutral damp → red guard; 3 presets
S8+
Perceptual Tone + Color Ref
LAB zoned tone curve; pseudo-LUT hue/chroma adjust; neutral-region protection
OUT
Final Finish & Export
sRGB OETF; exposure/contrast/temp/tint; grain + bloom + sharpening → PNG + JSON report

## Slide 8
STAGE 03 — AGENTIC AI REFINEMENT
Gemini-Powered Iterative Refinement
ClassifierAgent
Film Type Detection
Gemini VLM → JSON: film_type
Types: negative_35mm, negative_120, positive_35mm, positive_120
Fallback: aspect ratio + luma/saturation heuristics
PostProcessingAgent
13-Stage Negative Pipeline
Routes by film type to correct pipeline
Negative: density inversion → gray-world WB → LAB neutralization → CLAHE → vibrance → unsharp
Positive: lighter 7-stage pipeline
EvaluatorAgent
Quality Scoring & Param Tuning
9 metrics: gray_mean, clipping ratios, channel_spread, saturation, laplacian_variance
Gemini scores image 0–1 + autonomously tunes 14 parameters
Loop until score ≥ 0.75 or max iterations reached
Feedback Loop
if score < 0.75 → EvaluatorAgent suggests new params → PostProcessingAgent re-runs → EvaluatorAgent re-scores → repeat (max_iter)
Output: <stem>_processed.png + <stem>_meta.json (score, metrics, params, iteration log)

## Slide 9
QUALITY ASSURANCE
Evaluator Quality Metrics & 14 Tunable Parameters
gray_mean
Ideal: 100 – 165
Overall exposure level
gray_std
Ideal: > 30
Tonal contrast present
clipped_black
Ideal: < 0.5 %
No crushed shadows
clipped_white
Ideal: < 0.5 %
No blown highlights
blue_red_delta
Ideal: ≈ 0
Color balance neutral
channel_spread
Ideal: < 0.10
No dominant color cast
mean_saturation
Ideal: 0.08 – 0.45
Natural color richness
laplacian_var
Ideal: > 150
Image sharpness proxy
quality_score
Ideal: ≥ 0.75
Gemini VLM composite grade
14 Autonomously Tuned Parameters:
wb_clip_percent · black_point · white_point · clahe_clip · clahe_grid · unsharp_amount · unsharp_sigma · desat_strength · shadow_lift · gamma · lab_strength · highlight_compression · vibrance · desat_sigma

## Slide 10
TECHNICAL SUMMARY
From Film to Feed
40
tiles
feather-blended into
seamless mosaic
10+
stages
physically-grounded
RAW pipeline
14
params
tuned autonomously
by Gemini VLM
9
metrics
exposure, color,
sharpness, clipping
Scan → tile capture via RPi + STM32 Stitch → feather-blend 40 tiles Process → density inversion + AI refinement
ECE 445 · Film Digitization System · Post-Processing Team